## Slide 1
Principles of Digital Communications
Project presentation
Gaiëtan RENAULT Sophia ARTIOLI Alexandre SANTANGELO

## Slide 2
input.txt
EPFL Server
Channel
Transmitter
Receiver
output.txt
msg-received.txt
msg-to-send.txt
UTF-8, XOR, Hadamard encoding
Hadamard , XOR, UTF-8 decoding
Overall
X
Y

## Slide 3
input.txt
msg-to-send.txt
Transmitter
Chars to bytes
(UTF8)
Control bit encoding
Split sequence in two and apply XOR
---------------------------------------
Hadamard encoding with order
Pad entering sequ. with 0x0 (null char) so that we can map every bits sequences to bits sequence using Hadamard encoding.
Reshape
Map bits
Map 0 to -1 and 1 to 1
640 bits
~80 chars
960 bits
bits

## Slide 4
output.txt
input.txt
AWGN Channel
Server
Erease (periodically) one third of input, by mapping bit to 0. Then apply i.i.d Gaussian noise.

## Slide 5
msg-received.txt
output.txt
Receiver
Bytes to chars
(UTF8)
Control bit decoding
If necessary (J is 0 or 1) recover ereased 3-period values.
---------------------------------------
MAP estimation of J
Computing minimum argument above sum of absolute 3-period values. Then delete corresponding 3-period values.
Reshape
,…
Hadamard decoding with order
Map reals nbrs sequences to bits sequence using maximum argument inner product rule (decoded is closest one).
640 bits
~80 chars
nbrs
640 bits

## Slide 6
To finish
Works for all UTF-8 characters.
Hadamard coding ~ Orthogonal coding (problem 2 of GHW2) in fact.
8 bits order Hadamard was not sufficiently reliable, that’s why we’ve implemented 9 bits order Hadamard
Ideas to reduce total block length n < 60000 (channel parameter) :
As encoded length sequence exponentially increasing with order in Hadamard coding, one way to deal with it is to remove random bits of encoded sequence known to receiver after Hadamard coding (Heuristic way)
Implement other coding scheme (convolutional ? Too complex). We decided to also implement Random code (also in main.py), with it we can freely play with the block length. Using empirical method it seems that random code works fine with N = 370 and so a total block length of n = 44400 (better than Hadamard which has n = 55188)

## Slide 7
To finish
Test
Bibliography :
We based our thinking on Hadamard’s Coding Matrix and Some Decoding Methods paper.